DEPARTMENT:		Heating, Ventilation, Air Conditioning and Refrigeration

COURSE NUMBER:	HVAC/R 007

COURSE TITLE:		REFRIGERATION WELDING

WORKSHEET

| Course Objectives (not part of SLO-but derives SLO) | Outcome | Activity | Assessment |
| --- | --- | --- | --- |
| Recognize a backfire or flashback in gas welding and take corrective action; set up an oxy-acetylene torch and related equipment | Students will develop the ability to light a gas welding torch and adjust the flame to prevent a backfire or flashback from occurring. | Given an oxy-acetylene gas welding torch, each student will light and adjust the flame to the proper temperature while maintaining proper safety procedures. | Students will set up the oxy-acetylene welding torch and adjust the regulators to assure the proper supply of gases and light the torch and adjust the flame to neutral position to start welding thereby preventing a flashback from occurring. |
| Distinguish between neutral and oxidizing torch flames | Students will realize the importance of properly adjusting the gas torch to produce a neutral flame to correctly solder copper tubing. | Students will understand why the neutral flame is necessary to solder copper and the results obtained if the wrong flame is used. | After setting up a gas torch and lighting the torch to produce a neutral flame, students will solder a copper joint that is acceptable. |
| Carry a welding puddle with and without filler metal, in the flat position | Students will demonstrate the ability to use a torch to melt the base metal and fuse two pieces of metal with or without welding rod. | Students will demonstrate the ability to properly manipulate the welding torch to fusion weld a piece of carbon steel to produce a quality weld. | Students will weld a metal coupon and fuse the two pieces to complete a welded joint that is free of inclusions, porosity and is acceptable to American Welding Society (AWS) welding standards of visual inspection. |

SLO#1	Students will demonstrate the ability to properly set up and light a gas welding torch using all safety instructions and adjust the welding flame to produce a neutral welding cone that is free of flashbacks and backfires.

SLO#2	Students will demonstrate the ability to solder copper tubing using a properly adjusted gas welding torch to produce a joint that is visually accepted in accordance with AWS standards of quality.

SLO#3	Students will demonstrate the ability to weld a metal coupon and fuse the two pieces to complete a welded joint that is free of inclusions, porosity and is acceptable to AWS welding standards of visual inspection.